## Slide 1
Server
Server App
  Android app for Bluetooth communication between U3 and ZigBee
  Configuring nodes
    To local / remote nodes
      Set GPIO mode
      Read GPIO values
      Read AI values
      Set report mode (sampling / change)
      Set GPIO values
    Scan ZigBee devices
  Server for controlling the nodes
    TCP socket for connection
U3
Bluetooth
BT-ZigBee
Combo
Bluetooth
ZigBee
(Coordinator)
Device
ZigBee
(Device)
Switch, Relay
TCP
Server

## Slide 2: Configuring Nodes
Coordinator / Router / End-Device
  AT+NT=0, 1, 2, 3, 4
  0=none, 1=coordinator, 2=router, 3=end-device, 4=sleepy end-device
For coordinator, Permit Joining
  AT+PJ=255 (or sec)
Node name
  AT+NN=<value> (up to 16 chars)
Scanning
  AT+AS : scan network
  AT+ES : scan energy of the channels
  AT+DS : scan nodes in the current network
  AT+RS : showing RSSI and LQI RSSI=-100~+127dBm, LQI=0~255

## Slide 3: Configuring GPIOs
Mode setting
  AT+GPIO<number>=<value>
  0=disabled, 1=DIN, 2=DOUT(low), 3=DOUT(high), 4=AIN (9~14), 5=reserved
In / Out
  AT+DIO? or AT+DIO<number>?
  AT+DIO=<value> or AT+DIO<number>=<value>
Analog
  AT+AI? or AT+AI<number>?
  출력값을 실제 측정된 전압값으로 변환
    출력값이 0 ~ 7FFF 인 경우, Voltage (mV) = Value * 0.1
    출력값이 8000 ~ FFFF 인 경우 Voltage (mV) = (Value – 65536) * 0.1
  온도센서에서 실제 측정된 전압값을 온도로 변환
    Temperature(℃) ={ Volt(mV) -600(mV)} * 0.1(℃/mV)
  조도센서에서 실제 측정된 전압값을 조도로 변환
    Illumination(Lux) = Volt(mV) * 0.25(Lux/mV)

## Slide 4: Configuring GPIOs
Periodic Sampling
  AT+DL=<IEEE address>
  ATS42=<value> Sampling period (sec)
  ATS43=<value> 0 for DL, 1 for Sink node
  ATZ
  Data format : ++<IEEE address>|<GPIO value><CR>
Change Detection Sampling
  AT+DL=<IEEE address>
  ATS43=<value> 0 for DL, 1 for Sink node
  ATS44=<value> 0 for not using sampling
  ATZ

## Slide 5: Configuring BT-ZigBee Combo
Configuring as Coordinator
  AT+NT=1
  AT+NN=BT_ZIGBEE_COMBO
UI
  Configuring Node
    Node Type
    Node Name
  Configuring GPIO
    GPIO NO, PIN NO, MODE

## Slide 6: Client App
Query the devices
  Showing the devices configured by Server App
Attributes are shown as Icon
  Switches (R/W)
  Volume (R/W)
  Remote Control (R/W)
  Temperature (R)
  Luminance (R)
Send control and receive current status